## Slide 1: Reducing DRAM Latency via Charge-Level-Aware Look-Ahead Partial Restoration
Yaohua Wang, Arash Tavakkol, Lois Orosa, Saugata Ghose,
Nika Mansouri Ghiasi, Minesh Patel, Jeremie S. Kim,
Hasan Hassan, Mohammad Sadrosadati, Onur Mutlu
Notes: Hello, my name is Yaohua Wang and I will be talking about a mechanism to reduce DRAM latency

## Slide 2: Problem
DRAM access latency is a major bottleneck for system performance
Fundamental operations when accessing DRAM
Activation
Restoration
DRAM Cell
Row buffer
Refresh
Restoration latency takes up to 43.6% of DRAM access latency
Notes: DRAM Access Latency is a major bottleneck.
[click]
a DRAM chip consists of DRAM cells and the Row buffer. DRAM cells store data as charge in a capacitor.
[click]
When accessing data in DRAM.
[click]
Activation opens one of the DRAM rows, and copies the data into the row buffer to serve reads or writes.
[click]
As DRAM cells’ charge is drained during activation.
Restoration restores the charge to maintain the data integrity.
[click]
DRAM cells lose charge overtime.
[click]
To prevent data loss, DRAM cells are periodically refreshed.
[click]
Among these operations, the restoration operation is responsible for up to 43.6% of the total access latency.

## Slide 3: Motivation
Prior work applies partial restoration to soon-to-be-refreshed DRAM rows
Partial restoration can be applied to soon-to-be-reactivated DRAM rows
Observation:
a recently-accessed row is likely to be accessed again soon
Notes: Prior work can cut down the restoration time, by taking advantage of the fact that refreshes are regularly scheduled.
As a result, they apply partial restoration to soon-to-be-refreshed rows.
[click]
We observe that, due to the high temporal locality in DRAM access patterns, a recently accessed row is likely to be accessed again soon.
[click]
If we can predict the interval between consecutive accesses to a DRAM row, we can apply partial restoration to soon-to-be-reactivated rows. This can greatly increase the potential of partial restoration.

## Slide 4: Our Proposal
We propose charge-level-aware look-ahead partial restoration (CAL)
  CAL predicts the next access time at high accuracy (i.e., 98%)
  CAL applies partial restoration
    based on the predicted next access time
    ensuring high enough restoration level
    maintaining the benefits of latency reduction mechanisms for highly-charged rows
Notes: We propose: charge-level-aware look-ahead partial restoration.
it contains two important components:
[click]
First, we find that a row that had a short access-to-access interval before will likely have a short access-to-access interval again, based on this observation, CAL predicts the next access time at high accuracy, about 98% on average.
[click]
And then, CAL applies partial restoration
[click]
based on the predicted next access time
[click]
With enough charge level
[click]
to maintain the benefits of latency reduction mechanisms for highly-charged rows.

## Slide 5: Results
We comprehensively evaluate CAL using a wide variety of workloads and across many system and mechanism parameters
CAL is implemented fully within the memory controller without any changes to the DRAM module
14.7% performance improvement 11.3% energy reduction
Notes: According to our evaluation,
[click]
On average, CAL provides 14.7% performance improvement and 11.3% energy reduction.·
[click]
CAL is implemented fully within the memory controller and has very small hardware overhead.

## Slide 6: Reducing DRAM Latency via Charge-Level-Aware Look-Ahead Partial Restoration
Yaohua Wang, Arash Tavakkol, Lois Orosa, Saugata Ghose,
Nika Mansouri Ghiasi, Minesh Patel, Jeremie S. Kim,
Hasan Hassan, Mohammad Sadrosadati, Onur Mutlu
Session 3-A, Oct 22
Notes: Thank you.
Please come to my talk in session 3A.